## Slide 1: Warm-ups
Make a table showing all possibilities for entering a house through a door where there are two locks on the same door.
What does this table resemble?
Create a truth table for (p v q) ^ (~q)
Lock 1 | Lock 2 | Door
Locked | Locked | Locked
Locked | Unlocked | Locked
Unlocked | Locked | locked
Unlocked | Unlocked | unlocked
A table for p ^ q
P | Q | P v Q | ~Q | (pVq) ^~q
T | T | T | F | F
T | F | T | T | T
F | T | T | F | F
F | F | F | T | F

## Slide 2: Computer logic networks
Lesson 1.4
Goal for the day: Translate between logic networks and
logical expressions and construct input-output tables

## Slide 3: Example 1
Since the switch to 100% digital broadcasting in 2009, analog televisions need a converter box to receive a signal to view free TV. In order to see a picture, both the TV and the converter box must be on. Make a table for when the picture is on or off.
Television | Converter Box | Picture
Television | Converter Box | Picture
On | On | On
On | Off | Off
Off | On | Off
Off | Off | off
inputs
outputs

## Slide 4: New symbols – Logic Gates
and
or
not
Logic Gate: A device that
acts on input signals that it
receives to produce an
output signal (1 or 0).
True = 1
False = 0

## Slide 5: Example 2
P | Q | ~ q | P and ~ q | ~ (p and ~ q)
Construct an input-output table (truth table) that corresponds to the following network.
p
q
P | Q | ~q | P and ~ q | ~ (p and ~ q)
1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1

## Slide 6: Verify that this network is equivalent to the previous slide
P | Q | ~p | ~p pr q
p
q
P | Q | ~ p | ~p or q
1 | 1 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 1 | 1
0 | 0 | 1 | 1

## Slide 7: Find the logical expression that corresponds to the following network.
p
q
r
(~q ^ p) v r

## Slide 8: P v (~q ^ ~R)
p
q
r

## Slide 9: Homework
Page 36 – 38
6 – 18
Read/notes on 1.5